## Slide 1: Charge Exchange Spectroscopy of Multiply Charged Ions of Industrial and Astrophysical Interest
Hajime TANUMA
Department of Physics
Tokyo Metropolitan University
3rd October, 2012
ICAMDATA, NIST, USA

## Slide 2: Activity of Atomic Physics Group in TMU
Electrostatic Ion Storage Ring (E-ring)
Drift Tube
(ion swarm at 4.3 K)
RCE
(resonant coherent excitation)
ECRIS
(highly charged ions)
GeV
1 - 100 keV
0.5 - 100 meV
10 - 30 keV
H. Shiromaru, J. Matsumoto,
T. Azuma, T. Majima,
H. Tanuma, K. Hansen
T. Azuma (RIKEN)
H. Tanuma
H. Tanuma
Ion Mobility Spectrometry:
Detection of chemical warfare agents

## Slide 3: Contents of this talk
Charge Exchange Spectroscopy
Industrial part :
EUV lithography
Xe and Sn ions
Astrophysical part :
Solar Wind Charge Exchange
bare and H-like O, N, C ions
3

## Slide 4
“The number of transistors incorporated in a chip will
approximately double every 24 months.”
Gordon Moore, Intel Co-founder (1965)
Moore’s Law

## Slide 5
Light Sources for the Photo-Lithography
Hg lamp g-line = 436 nm ( -1989)
Hg lamp i-line = 365 nm (1990-1994)
KrF laser = 248 nm (1995-2002)
ArF laser = 193 nm (1994- )
Higher Integration = Shorter Wavelengh
What is the next ?
That is (was) EUV@13.5 nm !
That will be 6.x nm.

## Slide 6
max ~ 13.5nm
Reflectivity of Mo-Si multi-layer mirror
Light Source ? = Plasma of Xe or Sn
Principle of the EUV lithography
EUV = Extreme Ultra-Violet
( 13.5 nm = 91.8 eV )

## Slide 7
J. Phys. Chem. Ref. Data 33 (2004) 765-921.
No wavelengths or energy levels have been reported for Xe XII - Xe XVII.
Our strategy to obtain the atomic data on Xe ions :
Collision-induced EUV emission
Charge Exchange EUV Spectroscopy
Atomic data compilation by E. B. Saloman, NIST

## Slide 8
differential pumping
target gas
liq. N2 cooled CCD
TMP
TMP
PGIS = 3 x 10-3 Pa
PCC = 3 x 10-6 Pa
PCC < 1 x 10-3 Pa
↓ target gas
(He, Ar, Xe)
ECRIS
Xeq+, Snq+ ( i = 0.1 - 1eμA )
( E = 20q keV )
hν
CCD image
Grazing Incident Spectrometer
Experimental Setup
collision
center
Notes: 実験装置の概略図です．
ECRイオン源より引き出された多価Snイオンを，磁場で価数選別し，衝突領域に導きます．
衝突領域では標的気体と多価イオンが衝突し，電荷移行反応における発光を斜入射回折分光器で分光し，CCDに記録します．
標的気体としては主にHeとXeを用いました。
また，横軸はO5+やO6+の発光ラインを用いて波長校正をしました．
スペクトルの図でノイズか発光ラインかの判断が付きにくいものについては，最終的にこのCCDの画像より判断しました．
(Next Page)

## Slide 9
Experimental Results on Xeq+
( q = 7 - 18 )

## Slide 10
He gas target
Xe gas target
Emission of (q-1)+ ions

## Slide 11
Xe6+

## Slide 12
Emission lines of Xe6+ in the Saloman’s report
only 9 lines in 6 - 24 nm
( total 131 lines )

## Slide 13
Energy levels of Xe6+ in the Saloman’s report
72 levels give 72C2 = 2556 lines.

## Slide 14
Identification of emission lines of Xe6+
4 new transitions
Ground State : Xe6+ [Kr]4d105s2

## Slide 15
Summary of Xe spectra analysis :
Xe6+ : 4 lines, 4 new transitions
Xe7+ : 22 lines, 8 new transitions
Xe8+ : 39 lines, 9 new transitions
H. Tanuma et al., Phys. Rev. A 84 (2011) 042713.
q ≥ 9 : too many lines to identify perfectly for us
eg. UTA (un-resolved transition array)

## Slide 16
Average transition wavelengths
Systematic discrepancy in 4d-4f = Configuration interaction
(F. Koike)

## Slide 17
Experimental Results on Snq+
( q = 5 - 21 )

## Slide 18
H. Ohashi et al., J. Phys. B 43 (2010) 065204.
Snq+

## Slide 19
Collaborators in Industrial part :
experiment :
Dr. Hayato Ohashi (TMU → Univ. Electro-Communication)
Dr. Shinsuke Fujioka (ILE, Osaka Univ.)
Prof. Hiroaki Nishimura (ILE, Osaka Univ.)
theory :
Dr. Akira Sasaki (APR, JAERI)
Prof. Fumihiro Koike (Kitasato Univ.)
Prof. Katsunobu Nishihara (ILE, Osaka Univ.)
Dr. Rebekah D’Arcy (University College Dublin)
Prof. Gerry O’Sullivan (University College Dublin)
Acknowledgement :
This work financially supported in part by MIXT (Ministry of Education, Culture, Sports, Science and Technology, Japan) under contact subject
“Leading Project for EUV lithography source development”.

## Slide 20
Solar Wind = extremely thin plasma
- Negative : e- ~ 10 cm-3 around the Earth
- Positive : H+ ~ 95%
He2+ ~ 4%
Cq+, Oq+, Neq+, Mgq+, Siq+, Sq+ etc.
- Velocity : 200-400 km/s, 700-900 km/s
(0.21 - 4.2 keV/u)

## Slide 22
3/4 keV diffuse background map from the ROSAT all-sky survey.
At 3/4 keV, the sky is dominated by the relatively smooth extragalatic background and a limited number of bright extended Galactic object.

## Slide 23: Background soft X-ray by Suzaku
R. Fujimoto et al., Publ. Astron. Soc. Japan 59 (2007) S133–S140.
O6+(1s2-1s2p)
574 eV
O7+(1s-2p)
654 eV
Low resolution ~ 100 eV

## Slide 24: New experimental setup (1)
Switching
Magnet
14.25 GHz
ECR Ion Source
Analyzing
Magnet
Window-less
Silicon Drift Detector
(SDD)

## Slide 25: New experimental setup (2)
Magic Angle = 54.736°
Ion Beam
Collision Cell
target
gas inlet
to capacitance
manometer

## Slide 26: Experimental spectra in collisions of O8+ ions with H2 and He

## Slide 27: O8+ - He / H2 collisions
1s-np transitions of O7+, and 1s2-1s2p transition of O6+
2p > 4p > 3p
2p > 3p > 4p

## Slide 28: Comparison with theoretical calculations Atomic Orbital Close Coupling calculation by L. Liu & J. Wang

## Slide 29: Partial cross sections
Dominant capture level : n = 5 (H2), n = 4 (He)

## Slide 30: Cascade of transitions
n=5
n=4
n=3
n=2
n=1
Initial state distribution
2S1/2
2P1/2, 3/2
2D3/2, 5/2
2F5/2, 7/2
Notes: 電荷移行の初期分布がこのようになります。
このようにカスケードが起こり
発光します

## Slide 31: O8+ - He collisions
Agreement is almost perfect, except for 1s2-1s2p.
2p > 4p > 3p
2p > 4p > 3p

## Slide 32: O8+ - H2 collisions
2p > 3p > 5p > 4p
2p > 3p ~ 5p ~ 4p
Agreement is not sufficient, due to molecular structure (?)

## Slide 33: Cross Sections : O8+ - He
1s – np : E1
1s – 2s : M1, 2E1
difference
Preliminary Data

## Slide 34
Collaborators in Astrophysical part :
Atomic Physics Group, Tokyo Metropolitan University
H. Shimaya, T. Ishida, T. Kanda, S. Ishikawa, S. Suda
Astrophysics Group, Tokyo Metropolitan University
H. Akamatsu, Y. Ishisaki, T. Ohashi
JAXA / ISAS: K. Shinozaki, K. Mitsuda
IAPCM in Beijing: Ling Liu, Jianguo Wang
University of Electro-Communication: H. Ohashi, N. Nakamura
- Development of a new spectrometer
Sophia University: K. Okada
- Development of an ion trap

## Slide 35
What’s next?
Collaboration with National Institute for Fusion Science in Japan :
Charge exchange spectroscopy for W ions
Cross section measurements of W ions with He and H2 gas
Collaboration with Astrophysicists in Japan :
Systematic measurements of capture and emission cross sections
High-resolution spectroscopy for inter-combination lines
Measurements with an atomic hydrogen target
Observation of forbidden transitions of He-like ions by an ion trap
Introduction of a TES micro-calorimeter in our laboratory

## Slide 36
Thank you for your attention.
御静聴ありがとうございました。
謝謝